## Slide 1
International Spring School
Neustadt an der Weinstraße, Germany, March 10-14, 2025
Lab 1: Spherical harmonic synthesis
Marius Schlaak (TUM) & Grigorios Kalimeris (TUM)

## Slide 2
International Spring School Practicals
Four Practical Exercises on GRACE-FO Data Analysis:
Spherical Harmonic Analysis
Filtering/De-Striping
Global Analysis of EWH Grid Data
Regional Analysis

## Slide 3: Global Gravity potential Models (GGMs)
Static SH coefficients
GGMs consist of a set of spherical harmonic coefficients referring to certain and
„ICGEM format“: https://icgem.gfz-potsdam.de/docs/ICGEM-Format-2023.pdf
degree (L) order (M)
Spherical harmonic (SH) coefficients
standard deviation of SH coefficients
period [y]
t0 [yyyymmdd] : Reference epoch
Header section
Time variable
SH coefficients
Mandatory keywords

## Slide 4: Gravity & Normal potential
  Gravity potential (gravity field model – “true” Earth):
Normal potential (reference ellipsoid – model Earth):
Centrifugal potential:
Gravitational constant times
mass of the Earth
Radius of the sphere to which the SH series expansion of
the model refer
RModel + observation altitude; r=RModel on sphere’s surface
Fully normalized associated Legendre polynomials (of degree n and order m)
Fully normalized SH coefficients (of degree n and order m) = weighting of base functions
Normal gravitational potential
Gravitational potential
ω: angular velocity of the Earth’s rotation (precisely known quantity)
Common for both cases!
Maximum degree of model
Notes: • The geocentric coordinate r is called radial distance and is defined as the distance of the calculation point P from the geocenter.
• The geocentric coordinate θ is called colatitude (or polar distance) and is defined as the angle subtended between the position vector r and the Z-axis. The colatitude is reckoned clockwise from the Z-axis which is set as the colatitude reference of the geocentric spherical coordinates system.
• The geocentric coordinate λ is called longitude and is defined as the angle subtended between the projection of the position vector r onto the X-Y plane and the X-axis. The longitude is reckoned anticlockwise from the X-axis which is set as the longitude reference of the geocentric spherical coordinates system.

## Slide 5: Disturbing potential
  Disturbing potential:
    Deviation of the „true“ Earth from a model Earth (reference ellipsoid) in terms of gravity
    The SH coefficients of the normal potential U need to be scaled so as to correspond to the sphere with radius !
      See “reduce_normpot_grs80” function
Coefficient differences ()!

## Slide 6: Gravity functionals
The disturbing potential constitutes the basis for the computation of various gravity field functionals
  Geoid heights
  Height anomaly
  Gravity disturbances
  Gravity anomalies
  Vertical deflections
  Gravity gradients
  …
Notes: Can only be computed w.r.t. a defined geodetic reference system, e.g. the Geodetic Reference System 1980 (GRS80)

## Slide 7: Geoid heights
Geoid: Equipotential surface which poses the best approximation to the global mean sea surface
  Geoid height N: Deviation of geoid to reference ellipsoid; unit:
SH series expansion:
Approximation of normal gravity on the surface of the sphere:
normal gravity

## Slide 8: Gravity disturbances
Deviation between the norm of measured gravity and normal gravity in a point in space
  Gravity disturbance ; unit:
SH series expansion:

## Slide 9: Gravity gradients
Rate of change of gravitational attraction in a spatial direction
  Gravity gradient ; unit:
SH series expansion:

## Slide 10: Lab 1 – Goals
Become acquainted with different gravity functionals
Understand the impact of the degree of expansion
Understand the impact of observation altitude
Understand (roughly) the scale of the static gravity signal and its temporal variations

## Slide 11: Lab 1 Walkthrough – Task 1 (1)
Read gravity field model ITSG-GRACE2018s
  See “readicgem” function
Generate disturbing potential coefficients by subtracting the GRS80 normal potential
  See “reduce_normpot_grs80” function

## Slide 12: Lab 1 Walkthrough – Task 1 (2)
SH coefficients format
0
0
order m
order m
degree n
degree n
order m
degree n
order m
„CS-format“
„SC-format“

## Slide 13: Lab 1 Walkthrough – Task 2
Compute global geoid heights up to various maximum harmonic degrees
  See “shs” function
Plot (with coastlines!) and interpret your results
longitude & colatitude (parameters of shs)
lon=[0:360]°; col=[0:180]°
coastlines
(coast30.mat coast.npz)
global grid (output of shs)

## Slide 14: Lab 1 Walkthrough – Task 3
Compute and visualize global grids of gravity disturbances and vertical gravity gradients up to various maximum harmonic degrees (analogously to task 2)
  See “shs” function
How does the spatial signal change for each of the investigated gravity functionals? Why?
  See SH series expansion equations…

## Slide 15: Lab 1 Walkthrough – Task 4
How does the observable gravity signal change with increasing altitude? Compute and visualize gravity disturbances as seen from various satellite altitudes
  See “shs” function
  Based on your findings so far, which conclusions regarding altitude and observation technique can be drawn for a real gravity field mission?

## Slide 16: Lab 1 Walkthrough – Task 5
Import the gravity field model of April 2004 and visualize the corresponding geoid heights. Can you visually recognize any differences to the static model’s geoid heights?
Visualize this model’s deviation to the long-term mean (= static model). Do you notice anything specific about the signal’s behaviour?
  Generate model differences on coefficients level!

## Slide 17: Access to Practical Material
Instructions, Data, and Source Code are available on the Spring school website
https://www.asg.ed.tum.de/iapg/nerograv/spring-school/practicals/

## Slide 18: Appendix (1)
=
+
=
+
+
mean
zonal
sectorial
tesseral
=
=
-
+
+

## Slide 19: Appendix (2)
C00
C11
S11
C10
C20
C30
C40
S22
S21
S31
S33
S32
S41
S42
S44
S43
C21
C22
C31
C41
C32
C33
C42
C43
C44
C50
S51
S52
S54
S53
C51
C52
C53
C54
C55
S55
zonal
sectorial
sectorial
tesseral
tesseral
…
…
…
…
order m
order m
degree n